## Slide 1: Security for Ad Hoc Networks
Jun Tao

## Slide 2: Ad Hoc Networks
Ad hoc -- a Latin phrase which means
"for this [purpose]".
An autonomous system of mobile hosts
connected by wireless links, often called
Mobile Ad hoc NETworks (MANETs)

## Slide 3: Characteristics
No fixed infrastructure
Dynamic changing topology
  Mobile devices join/leave the network unexpectedly; they can also move freely
Energy-constrained
Limited bandwidth
Each node also serves as router
  Help to relay packets received from neighbors
Interoperation with the Internet

## Slide 4: Comparison
MANETs vs. Wired networks
  In MANETs, each node also works as router for forwarding packets
  In wired networks, routers perform routing task
MANETs vs. Managed wireless networks
  No infrastructure in MANETs
  Special node known as access point (AP) in managed wireless networks

## Slide 5: A MANET Example

## Slide 6: Mobile Devices
Laptop computers
Pagers, cellular phones, PDAs
In-car navigators -Dash Express
  Dash units talk to each other and form a network that connects to the Internet
  Traffic speed data is sent back to the company, then broadcast back to all local dash units
Sensors
……

## Slide 7: Wireless Sensor Network (WSN)
An emerging application area for MANETs
A collection of cheap to manufacture, stationary, tiny sensors
Network lifetime -- power as a major driving issue
Battlefield surveillance, environment monitoring, health care, etc.

## Slide 8: WSN Example

## Slide 9: Other MANETs applications
Collaborative work
Crisis-management applications
Personal Area Networking (PAN)

## Slide 10: Security Requirements in MANETs
Availability
Authorization and Key Management
Data Confidentiality
Data Integrity
Non-repudiation

## Slide 11: Security Solution Constraints
Lightweight
Decentralized
Reactive
Fault-tolerant

## Slide 12: Challenges
No infrastructure
Peer-to-peer architecture with multihop routing
Mobile device physical vulnerability
Stringent resource constraints
Wireless medium
Node mobility

## Slide 13: Security Issues

## Slide 14: Threats
Attacks
  External attacks
  Internal attacks
  Passive attacks
  Active attacks
Misbehavior

## Slide 15: MANETs Security
Routing security
Data forwarding security
Link layer security
Key management
Intrusion detection systems (IDSs)

## Slide 16: Routing in MANETs
Nodes’ mobility -topology changes rapidly
Large network size -significant amount of network control traffic

## Slide 17: MANET Routing Protocols
Topology-based approaches
  Proactive routing (table driven)
  Reactive routing (on demand)
  Hybrid routing
Position-based approaches

## Slide 18: Comparison
Proactive routing
  Classic routing strategies: link state, distance vector
  Keep track of routes to all possible destinations
  Changes in link connection updated periodically
  Minimal delay but substantial fraction of control information
  E.g. DSDV, WRP, TBRPF, OLSR, etc.

## Slide 19: Comparison
Reactive routing
  Only discover routes to destinations ondemand
  Consume much less bandwidth but experience substantial delay
  E.g. DSR, ADOV, TORA, etc.

## Slide 20: DSR vs. AODV
Dynamic source routing (DSR)
  Source broadcasts RREQ through the network
  Intermediate nodes add its addr to RREQ and continue broadcasting until RREP received
  Full path chosen by source and put into each packet sent
Ad hoc on-demand distance vector (AOVD)
  Hop-by-hop routing
  Source sends RREQ to neighbors
  Each neighbor does so until reach the destination
  Destination node sends RREP follow the reverse path
  Source doesn’t put whole path but only next hop addr in outgoing packets

## Slide 21: Routing Protocol Attacks
Attacks using modification
  Redirection by modifying route sequence number
  Redirection by modifying hop count
  Source route modification
  Tunneling

## Slide 22: Routing Protocol Attacks
Attacks using fabrication
  Falsifying route errors
  Broadcast falsified routes
Spoofing attacks
Rushing attacks

## Slide 23: Solutions to Secure Routing Protocols

## Slide 24: Data Forwarding Security
Threats
  Eavesdropping (passive attacks)
    cryptography can help to prevent but how to detect eavesdropping is still an open research topic
  Dropping data packets (similar to selfishness)
  Selfish behavior on data forwarding
    Drops other nodes’ packets to preserve its resources, e.g. battery power

## Slide 25: Detection Solution against Selfishness
End-to-end feedbacks
Monitoring in promiscuous mode (watchdog)
Activity-based overhearing
Mutually according admission in neighborhood
Reputation based solution
Probing

## Slide 26: Preventive Solution against Selfishness
Nuglets
  Nodes who use the service must pay for it to nodes that provide the service
Data dispersal
  Adding redundancy to the messages to send; thus partial reception can lead to successful reconstruction of messages

## Slide 27: Link Layer Security
IEEE 802.11 MAC
  Vulnerable to DoS attacks
  Attacks can exploit its binary exponential backoff scheme to launch DoS
  A security extension to 802.11 was proposed
    Backoff time at the sender is provided by the receiver
IEEE 802.11 WEP -discussed in wireless security

## Slide 28: Key Management
Most of the solutions for secure routing and data forwarding rely on cryptography
Key management is problematic because of the lack of any central infrastructure
  Private key infrastructure
  Public key infrastructure

## Slide 29: Private Key Infrastructure

## Slide 30: Public Key Infrastructure

## Slide 31: Intrusion Detection Systems (IDSs)
Proactive solutions cannot eliminate attacks (secure routing layer, link layer mechanism)
IDS presents a second wall of defense
Assumptions
  User and programs are observable
  Normal and intrusion activities can be distinguished

## Slide 32: Problems with Traditional IDSs in MANETs
Infrastructureless nature of MANETs
  No traffic concentration points for monitoring
Resource limitation of mobile devices
Lack of clear separation between normalcy and anomaly
  as nodes move around, the topology changes;
  so each node should expect different traffic pattern from its neighbors

## Slide 33: Proposed Solutions
Distributed, host-based, anomalybased, and cooperative

## Slide 34: Wireless Sensor Network (WSN) Security
Consists of thousands or millions of tiny devices:
  signal processing circuit,
  micro-controller,
  wireless transmitter/receiver,
  embedded sensor

## Slide 35: More Stringent Performance Requirement
More stringent performance requirement
  Energy efficiency -network lifetime
  Auto-organization
  Scalability to a high number of nodes

## Slide 36: Security Issues
Key distribution and management
  Scalable to a large number of sensor nodes
  Remains to be unsolved
    Key pre-deployment
    Shared key discovery
    Path-key establishment
  Alternatives
    Probabilistic key sharing protocols

## Slide 37: More Issues
Secure routing
  Most routing protocols are quite simple in WSN, thus more vulnerable to attacks. Some new attacks are:
    Sinkhole attacks
    Hello flood attacks
  Solutions
    SPINS -two building block security protocols: SNEP and μTESLA
    INSENS -intrusion-tolerant routing protocol

## Slide 38: More Issues
Secure data aggregation
  Key theme in design and development of WSNs
  Aggregators collect raw data, process it locally, and forward only the result to end-user
  Aggregation can take in any places, and must be secured
Denial of service
  Jammed by adversaries: jam the entire network by broadcasting a high enough energy signal
Resilience to node capture

## Slide 39: Summary
What we have discussed
  Characteristics of MANETs, WSNs
  Security issues in MANETs and WSNs
MANETs is a growth area of research; the security issues in MANETs attract a lot of researchers; we’ll be definitely seeing more of these problems in near future.

## Slide 40
THANK YOU !